Poll gearbox bitmask
and current state
Poll gearbox bitmask
and current state
Target gear
Right [Yellow]
Yes
Gear change
in progress?
Yes
No
Target gear
Left [Red]
No
Yes
Is spindle stopped?
No
No
Yes
Target gear
Mid [Blue]
Compare
commanded
speed with current
[Stage]_
LEFT_CENTER
Is on
Gearchange required?
Turn CW
(Reverse_Direction Off)
Turn CCW
(Reverse_Direction on)
Yes
No
Exit
No
Yes
Energise
Gear_change_start
End twitching
Delay 100ms
Delay 100ms
Deenergise
Gear_change_start
Determine nearest
gear speed
Write target
bitmask
Report current
gearbox speed
Spindle_stopped?
Exit
E-Stop
No
No
Yes
Do twitching
Commanded
Speed = 0?
Yes
No
Next stage
Input stage state?
Back gear
stage state?
Target bitmask
reached?
Target bitmask
reached?
On
Back-gear
Input
Input
No
On
No
Yes
Off
Mid
Yes
Off
Change req'd?
Change req'd?
Deenergise
Reverse_Direction
Gear_Motor_Back_Gear
Target bitmask
reached?
Mid stage state?
Deenergise
Reverse_Direction
Gear_Motor_Input
No
No
On
No
Yes
Yes
Off
Yes
Reverse
direction of rotation
of stage required?
Change req'd?
Reverse
direction of rotation
of stage required?
Deenergise
Reverse_Direction
Gear_Motor_Mid
State „OFF“
No
No
No
Yes
Yes
Yes
Energise
Reverse_Direction
Energise
Reverse_Direction
Reverse
direction of rotation
of stage required?
No
Delay 100ms
Delay 100ms
Yes
Energise
Reverse_Direction
Energise
Gear_Motor_Back_gear
Energise
Gear_Motor_Input
Delay 100ms
Backgear stage
state: on
Input stage
state: on
Energise
Gear_Motor_Mid
Exit
Exit
Mid stage
state: on
Exit